Coloring Your Woodturnings

Duane Hill

Jan 2011

Coloring in General

Coloring can take many forms

Staining

Stains are made up a larger particles and essentially stay on the surface or slight penetration of the wood

Dyeing

Dyes are made up of small particles that totally dissolve in their solvent; thereby getting much deeper penetration

Dye solvents are typically water or denatured alcohol

Aniline dyes may be dissolved in water or alcohol, check specific dye for dissolving agent

Inks are considered dyes

India ink makes a great black

Leather  dyes also work well

Painting

Larger particles, stays on surface

Can be opaque or transparent

Transparent lets grain show through

Markers

Typically alcohol based

Prismacolor

Craft Supplies

Sharpies

Pam uses these for coloring her pieces

Make sure the form is perfect and the surface has no flaws; coloring will bring out the flaws

Additional materials

Gloves

Smock for clothes

Glass jars

Eye droppers

Color wheel

Pallet

Paper towels

Air compressor for air brushing

Air brush

Masking

Good for limiting where dye/paint goes

Masking fluids

Latex

Stuff like rubber cement

Sign mask

Can be sprayed on or brushed on

Best for non-consistent diameters

Frisket

Could for consistent diameters

Can be cut with Xacto knife

Woodburning makes an effective and decorative mask

Dyeing

Preparation

Sanding

Sand to no finer that 320 grit

Much finer and the ends of the wood fibers get burnished over and the dye won’t penetrate

Seal the surface with thinned shellac

Option, depending on wood and thickness

Seal inside surface to greatly reduce bleed through

Seal both surfaces (inside and out) for best bleed through protection

Seal top surface if using a mask

Lightly sand after sealing (320 grit)

Apply first layer of dye

Apply darker colors first

Can be brushed on or dabbed on with paper towel

Allow it to dry

Lightly sand with 320 grit.

Can sand through in areas, if desired

Apply other dye layers

Can cover all or in spots

Sand with 320 grit

Remove masking

Sand to 400 and finer grits

Apply finish

I like to use an oil finish for first two or three coats and then add a poly as a top coat

Other Notes

Use blue as a first dye color if dyeing black

Without blue, the black takes on a bronze cast

Can dilute dye with either alcohol or water

Final coat is a “wash”, highly diluted dye

Can mix colors

Use eye dropper to retrieve dye

One dropper per color

Count drops of each dye and record

Use pallet or glass jar to mix in

Painting

Preparation

Sand to final grit

Define paint area

Carve

Woodburn

Masking

Apply paint

Brush

Air brush

Final sanding

Apply finish

Markers

Preparation

Sand to final grit

Outline areas to be colored with woodburning

Color areas with markers

Apply fixative

Avoid alcohol finishes

Apply finish